## Slide 1
Time Compare Unit Update
For Lockheed Martin
Design Review
March 01, 2019

## Slide 2: The Lockheed Time Unit
  Chris Tota (Logistics manager)
  Connor Granaas (Design manager)
  Rodney Rodriguez (Project manager)
  Nate Kilmer (Communications / Finance manager)
  Jacob Doyle (Test manager)
  Customer: Rhett Rodewald (Lockheed Martin)
  Faculty Advisor: Dr. Byeong Lee

## Slide 3: Project Background
  Customer:
  Specializes in
    Global Aerospace
    Defense
    Security
  TCU Solution
    To aid in satellite and ground station communication
    Besides the device I/O, team will focus on the unit itself, disregarding the future environment at LM.
(since 1995)

## Slide 4
Problem statement
Time Compare Unit Functionality
  Receive two 1pps signals from coax
  Compute Δt, minimum accuracy 100ns
  Output Δt over ethernet
Ground
Station
Satellite
Satellite Signal
Reference Signal
Time Compare Unit
-Computes
Δt = tgr - tsat
-Outputs Δt
Δt
Client Computer
Receive and Display
Coax Cable
Coax Cable
Ethernet

## Slide 5: Timing Diagram
Signal 1 (Reference Signal)
1s
Voltage (V)
Voltage (V)
Time (s)
Time (s)
5
0
0
5
~1s
Signal 2 (Satellite Signal)

## Slide 6: Timing Diagram
Voltage (V)
Voltage (V)
Time (s)
Time (s)
5
0
0
5
Signal 2
Signal 1

## Slide 7: Timing Diagram
Voltage (V)
Voltage (V)
Time (s)
Time (s)
5
0
0
5
Signal 2
Signal 1

## Slide 8: Timing Diagram
Voltage (V)
Voltage (V)
Time (s)
Time (s)
5
0
0
5
Signal 2
Signal 1

## Slide 9: Timing Diagram
Voltage (V)
Voltage (V)
Time (s)
Time (s)
5
0
0
5
Signal 2
Signal 1

## Slide 10: Timing Diagram
Signal 2
Voltage (V)
Voltage (V)
Time (s)
Time (s)
5
0
0
5
Signal 1

## Slide 11: Changes to Proposal
  Platform has been selected
    Team has chosen to no longer pursue the FPGA or Sampling approach.
    A logic latch-timer method has been selected
  Other than selecting a design method
    The team’s proposal has remained the same

## Slide 12: Changes to Requirements
  Team must now consider
    The TCU outputting a ∆t = 0 (picoseconds)
    Two signals coming in at the same time
  Solution
    The team plans to account for this change in the software that will be uploaded to the micro controller.
Software
Hardware

## Slide 13: Existing Specifications
Constraint | Unit | Minimum | Typical | Maximum
Operating Temperature | °C | 15 | 20 | 30
Cost | $ | - | - | 5000
Input High | V | 4.5 | 5.0 | 5.5
Input Low | V | -0.5 | 0 | 0.5
Input Pulse Width(Ground) | μs | 90 | 100 | 110
Input Pulse Width(Satellite) | μs | 19.99 | 20 | 20.01

## Slide 14: Existing Specifications
Constraint | Unit | Minimum | Typical | Maximum
Supplied Power | V | 11.5 | 12 | 12.5
Rise Time | ns | - | - | 50
Calculation Time | s | - | - | 1

## Slide 15: Changes to Specifications
  SAM E70 - IwIP
  Logical Components
  OCXO Oscillator
  - ECOC-2522

## Slide 16: Timing Errors
From last presentation:
  Rise Time Error:
  Clock Resolution Error:
  Frequency Stability (5ppb):
Recently discovered:
  Switch Turn-on Time Error:
    Only relevant when
  Logic Timing Error:
    1 to 4 ns (varies part to part)
Guaranteed Error:

## Slide 17: Time Compare Unit - Design
  Basic Functionality:
Clock
Latch
System
Calibration
Latch
System
Counter 1
Counter 2
Micro-
Controller
Signal 1
Signal 2

## Slide 18: Design Implementations
  Design 1
    Measures the time difference between the signals, no matter which signal came in first
    If signal 2 before signal 1 
  Design 2
    Measures the actual time difference between the signals, with signal 1 as the reference

## Slide 19: Design 1
Signal 1
Signal 2
Voltage (V)
Time (s)
Time (s)
5
0
0
5
= 1 -
Voltage (V)

## Slide 20: Design 2
Signal 1
Signal 2
Time (s)
Time (s)
5
0
0
5
=
Voltage (V)
Voltage (V)

## Slide 21: Design 1 - Measurement Circuit
Delay = 10ns
FEP = Falling Edge Pulse

## Slide 22: Design 1
Signal 1
Voltage (V)
5
0
Signal 2
Voltage (V)
5
0
Switch Control
Voltage (V)
5
0
Switch
Control

## Slide 23: Falling Edge Pulse (FEP) Circuit
Input
5
Q
5
Voltage (V)
Delay = 20ns
Voltage (V)

## Slide 24: Design 1 - Did Signal 2 Come in First
Delay = 10ns

## Slide 25: Measurement Circuit – Design 2
Delay = 10us

## Slide 26: Design 2 Methodology

## Slide 27: Design 1 & 2 - Calibration Circuit
Calibration every 2 seconds

## Slide 28: Pros & Cons
 | Pros | Cons
Design 1 | No counter value storage | An additional counter
 | No missed counts | More components
 | Meets specifications | 
Design 2 | Fewer components | Counter value storage
 | Less switching delay | Possible missed counts
 | Meets specifications | 

## Slide 29: Microcontroller-Hardware Interface
  74lv8154 contains two 16-bit counters
  Counters will be cascaded to achieve 32 bits
  Counter data is accessed by byte through 4 control lines (one-hot encoding)

## Slide 30: Measurement Buffering
Time (s)
0
1
Active-high
count ready
  Measurement completes at any point in 1Hz cycle
  May leave little room for reading counters
  Counter output will have to be buffered

## Slide 31: Oscillator Calibration
  Ground station provides a consistent 1pps that will act as a reference
  This Ground Station signal is at the top of the calibration hierarchy
  Calibration is performed through a counter that increments on every OCXO clock pulse
  Calibration counter is read every other pps

## Slide 32: Oscillator Calibration
Time (ns)
50
100
Nominal Rate
Measured Rate
9 cycles
10 cycles
Oscillator Output

## Slide 33: Software Flowchart
  Initialization
  Set up the µC I/O and TCP/IP stack
  Warmup
  Wait for OCXO to stabilize Calibration
  Read calibration counter, calculate calibration factor Measurement
  Read measurement counter, apply calibration factor
  Network
  Send the measurement to the client

## Slide 34: Hardware Characteristics
Testing components individually
  Need to characterize how individual components respond to inputs
  Slowly piece together unit, maintaining desirable characteristics
  Translate complete unit to solderable breadboard once a functional unit is assembled

## Slide 35: Testing Plan: Concept
Produce a series of known deltas
  Two signal sweep
    Set sig1 to 1Hz
    Set sig2 to 0.99Hz  deltas increase by 10,101,010ns
      e.g. Δt1=10,101,010ns, Δt2=20,202,020ns, Δt3=30,303,030ns, etc.
    Compare measured deltas to predicted values

## Slide 36: Testing Plan: Equipment
Produce a series of known deltas
  Keysight 33622A
    High-stability timebase: 0.1ppm stability
    Low jitter: ~1ps jitter
    Low harmonic distortion: ~0.03%
    Pulses up to 100MHz
  Keysight MSOX6004A Oscilloscope
  Agilent N2894-60002 Passive Probe
    700MHz

## Slide 37: Testing Plan: Equipment

## Slide 38: Testing Plan: Expected Results

## Slide 39: Testing Plan: Expected Results

## Slide 40: Testing Plan: Expected Results

## Slide 41: Testing Plan: Live Demo
Live Stress Tests
  Conduct series of specifically designed, troublesome scenarios
  Predict measurement values
  Confirm the integrity of our measurements

## Slide 42: Deliverables: Hardware
  SAM E70 headers mechanically compatible with Arduinio
  Hardware will rest on shield above the SAM E70 board

## Slide 43: Deliverables: Software
  Data is presented through a telnet client
  Delta will be reported in 10’s of nanoseconds
  Typical measurement message is a 22-byte ASCII string
  Point-to-point network

## Slide 44: Integrated Course Knowledge (Review)
Course Number: | Course Name: | Reason:
ECE 1411 & 2411 | Logic Circuits I & II | Logic gates and digital circuits
ECE 2205 & 3205 | Circuits and Systems I & II | Introduction to passive components and AC/DC circuit analysis
ECE 3210 & 3230 | Electronics I & II | Introduction to active components in AC/DC analysis
ECE 3430 | Intro to Microcomputer Systems | Interfacing with software driven hardware (μC’s)
ECE 4510 | Feedback Control Systems | Simulation modelling (software)

## Slide 45: Gantt Chart Table

## Slide 46: Gantt Chart

## Slide 47: Project Budget $5000
  $5000 - $523.40 = $4476.60 Remaining
Component | Part Number | Qty. | Unit Cost | Total
100MHz Oven Controlled Oscillators | ECOC-2522 | 2 | $116.68 | $233.36
SAM E70 Microcontroller | ATSAME70-XPLD | 1 | $40.83 | $40.83
JK Flip Flops | SN74F109N | 15 | $0.779 | $11.69
D Flip Flops | 74AC11074N | 15 | $1.895 | $28.43
SR Latches | SN74LS279AN | 15 | $1.174 | $17.61
32-bit Counters | SN74LV8154 | 15 | $1.090 | $16.35
XOR Gates | SN74AHC86N | 15 | $0.341 | $5.12
NOR Gates | SN74AS02N | 15 | $2.210 | $33.15
Inverters | SN74F04N | 15 | $0.559 | $8.39
SPDT Switches | TS5A9411DCKR | 10 | $0.545 | $5.45
Surface Mount to Through Hole Mounts | AN0002 | 10 | $2.690 | $26.90
Solderable Breadboards | PRT-12699 | 4 | $8.950 | $35.80
Shipping/Tax: |  |  |  | $60.32
TOTAL: |  |  |  | $523.40

## Slide 48: Summary
  - LTU is on track to deliver a working prototype of the time compare unit
  -The team plans on finishing hardware characterization and system prototyping to move to finalization stages

## Slide 49: Thank You
  Are there any questions?

## Slide 50: Setup/Hold Time for Design 1
  Our = 100MHz
  Our > 20µs
  Our = 10ns

## Slide 51: Design 1 Expanded